Table of Contents
Hardware interface	3
SPI messages	3
LoRa Fabian Arduino Library	4
begin (name)	4
begin (name, gateway_mac)	4
available ()	4
write (value)	4
write (buffer, length)	5
print (data)	5
println (data)	5
read ()	5
flush ()	5
stop()	5
Arduino example:	6

  1. Hardware interface

LoRa Fabian shield is connected to “Arduino UNO R3 connector”.
SPI is used to communicate with the shield:
- Arduino is SPI master.
- Same pin-out is used as for classical Ethernet Arduino shield:
  - Arduino pin 13: SCK
  - Arduino pin 12: MISO
  - Arduino pin 11: MOSI
  - Arduino pin 10: SS

Note: Using the same pin-out, will help makers to easily switch from Ethernet shield to a LoRa one.

SPI clock rate: 500kHz

IMPORTANT NOTE: LoRa shield application processor only runs at 8MHz while Arduino uno runs at 16MHz. So it is important to respect some timings on SPI bus to be sure the program receiving frames behaves correctly:
- Minimum wait time between SPI message: 160 us
- Minimum wait time between two bytes in a SPI message: 15 us

  1. SPI messages

Messages sent from Arduino, MOSI line:
Command	Length_msb	Length_lsb	[Params]/[Msg]	...

- Command: Command number (example: begin, available, write, read …). 1 byte.
- Length: Message length (not including command and length fields). 2 bytes.
- Params: A given command can have associated parameters. Optional field.
- Msg: A given command can have a message associated. Optional field.

Messages received from the shield, MISO line:

Previous Command Status	Shield status	[Byte Read]/[Available length_msb]	[Available lenght_lsb]

- Previous Command Status: Every command returns a status. As it is not possible to return a command status when the command is received for many commands, the status of command is sent during the next SPI message. 1 byte.
- Shield Status: Indicate the state of the shield. 1 byte.
- Byte Read: On Read command the byte read is returned. Only for Read command. 1 byte.
- Available: On Available command, two bytes are returned to indicate the number of bytes available in the RX buffer. 2 bytes.
  1. LoRa Fabian Arduino Library

The library is inspired from the Ethernet Arduino Shield library. The goal is to ease maker understanding and access to the shield functionalities.

LoRaFabian class will include functions:
    1. begin (name)
This function tries to attach to a gateway from the LoRaFabian network. It is blocking while the attach procedure is not complete.
Parameters:
  - name: string describing name of the node, example: "toto.ltn22.rennes.fablabnet.fr"

    1. begin (name, gateway_mac)
This function tries to attach to a specific gateway indicating its LoRa mac address. It is blocking while the attach procedure is not complete.
Parameters:
  - name: string describing name of the node, example: "toto.ltn22.rennes.fablabnet.fr"
  - gateway_mac: LoRa mac address of the gateway.

    1. available ()
Returns the number of bytes received by the shield.
Parameters:
None

    1. write (value)
Send a single byte to the gateway.
Parameters:
- value: int or char. 1 byte

    1. write (buffer, length)
Send a buffer of byte to the gateway.
Parameters:
  - buffer: bytes to send
  - length: buffer length
    - print (data)
Send a string to the gateway.
Parameters :
  - data: string to send.

    1. println (data)
Send a string to the gateway immediately followed by a newline.
Parameters :
  - data: string to send.

    1. read ()
Return the next byte or character received by the shield, or -1 if none is available.
Parameters:
None

    1. flush ()
Flush the RX buffer.
Parameters:
None.

    1. stop()
Close the connection with the gateway.
Parameters:
None.

    1. Arduino example:

#include <LoRa.h>

LoRaFabian lora;

const unsigned long requestInterval = 60000; // delay
unsigned long lastAttemptTime = 0; // last time you sent a message

void setup() {
 // Open serial communications and wait for port to open:
  Serial.begin(9600);

  LoRa.begin(“toto.ltn22.rennes.fablabnet.fr”);

  Serial.println("LoRa module starting...");
}

void loop()
{
  // if there are incoming bytes available:
  if (lora.available()) {
    char c = lora.read();
    Serial.print(c);
  }
  else if (millis() - lastAttemptTime > requestInterval)
    sendSensorValue();
}

void sendSensorValue() {
  // attempt to connect, and wait a millisecond:
  Serial.println("sending sensor value...");
  lora.write('D');

  // note the time of this connect attempt:
  lastAttemptTime = millis();
}